## Slide 1: LICAD 11
Choose menu language
Design of hanger support
Setup specifications
Setup project properties
Create DXF files
Create summary parts list

## Slide 3
Drawings and materials lists are always given out in the language set at the time.
Drawings which have been saved can be printed out in any of the languages
named above. Just make the appropriate setting before printing.
Select one of 12 languages

## Slide 4
Select Projects at first
Setup project properties

## Slide 5
Create your first Project
Enter a strong Project name
and use the other fields to
descripe your Project
Please confirm with Yes to activate your new project

## Slide 6
Your new project appears now in the
list box. The ident number is 72. This
number is for internal use only
You can leave the window via the
Exit button
Or you can change the project:
Click to a list box item
And click to the Select button

## Slide 7
Select a hanger configuration out of
The selection table
You will see this screen after choosen the
Designer button in the main window
Select ‚Static‘ to design spring hangers
Choose a simple hanger with a spring can
Double click to the picture to select the
configuration and to close the window
Design of hanger support

## Slide 8
Enter now the design parameters
Enter a distance fro m bottom of steel to the centre of pipe
200
A Hanger mark number
Enter now few values for
Load,
Diameter of pipe,
Insulation thickness,
Temperature of pipe,
And vertical movement
That‘s it
Click here to proceed

## Slide 9
Use those buttons to change different
orientation option

## Slide 10
Setup specifications
The most important information at a glance
Click here to enter setup

## Slide 11
Enter project information
here
Enable that to use this
feature

## Slide 12
Those values are important for the
selection of hangers. Change of
valuse could cause a different hanger
Type.
Use the fast selection buttons
For the most important rules

## Slide 13
Whether the operating load or the cold load is entered is of
special importance for the selection of variable spring hangers.
LICAD calculates each opposite load case and puts these out in
the drawing. Furthermore, the preset load of the hanger is put
out. The preset load consists of the cold load and the additional
load of the component which encloses the pipe.
This option prevents selection of clamp bases designed for the
temperature range up to 350°C/660°F (Material S235, S355).
The idea behind this is that even at lower temperatures and
comparatively smaller insulation thickness, clamp bases with
higher installation dimensions can be selected.
It has proved expedient to limit the length of threaded rods for the
transport of supports to sites. For design purposes the maximum length
of threaded rods can therefore be limited to 2000 mm. 3000 mm is
chosen as standard, 12 feet in UNC.

## Slide 14
These properties should not be set as default
Seated constant or spring hangers are supplied with supports
or base plates as standard. If so desired, these seated hangers
can also be supplied without these components, whereby constant
and spring hangers are seated directly on the housing.

## Slide 15
These properties should be set (recommended)
Password security is optional and need not be activated!

## Slide 16
The option “Side view” controls whether,
when printing, a second view appears with
the printout. This is however not available
for all configurations.
Print-outs can be made in various languages
independently of the menu language selected.
The choice of languages depends not on the
operation system but on the printer.

## Slide 18
Create DXF files
Open Setup window at first to configure DXF settings

## Slide 19
Create DXF files
Enter a Layer name,
a value for Text color and
Text height
Repeat for all other positions

## Slide 20
Create DXF files
In case to export graphic only
disable Apply options box
Choose paper size next.
Use combobox for defaults
Save settings & exit

## Slide 21
Create DXF files
Select drawings from the left box
And send them to the right box
Choose the correct folder for the DXF files
By default the Hanger mark number is used as file name.
Choose LICAD drawing number to get a numeric file name.

## Slide 22
Create summary parts list
Choose Summary button here

## Slide 23
Create summary parts list
Select drawings from the left box
And send them to the right box
Click to GO to start process

## Slide 24
Create summary parts list
Use either TXT or EXCL buttons to export the result
Choose here to get a preview
To get a further page with used drawing numbers
activate this box before starting the process